## Slide 1: Air quality monitoring through sensor-based networks in large metropolitan areas: The case of Athens, Greece
Dr. Georgios Grivas
Research Fellow, National Observatory of Athens (IERSD/NOA)

## Slide 2: Dense Air Quality Monitoring Networks in major European cities
No. of stations: ≈ 120
No. of stations: ≈ 70
No. of stations: ≈ 50
No. of stations: ≈ 50

## Slide 3: A less dense Air Quality Monitoring Network in a major European City
GREATER AREA OF ATHENS (GAA)
Population: 3.6 mil. (2019 – Eurostat)
Area: 412 km2 (Athens Basin)
Regional Units: 8
Municipalities: 56
Population Range: 18-664k (by municipality)
Density Range: 0.1-21.2 k/km2 (by municipality)

## Slide 4: Local factors exacerbating common European AQ issues
Wintertime “smog” due to residential wood-burning
  Research studies feature Athens as the biomass-burning capital of the EU
  Extreme short-term levels for PM2.5 (>200 μgm-3, hourly), with high contributions of organic compounds and black carbon
  Summertime photochemical smog
  High ozone levels with frequent exceedances of alert and information thresholds
  The majority of urban background sites in the GAA each year breach the annual EU target-value
  Aging vehicle fleet – Surge of diesel-powered cars
  A ban on private diesel cars ended in 2011, and they have since dominated new and used-car sales
  Greece has one of the most aged vehicle fleets in the EU (4th most aged for private cars, 1st most aged for trucks)
  Persistent AQ-standard violations for NO2, PM10 at traffic sites
  Shipping emissions
  Piraeus in the GAA is the busiest European passenger port and the 2nd most busy port in the Mediterranean

## Slide 5: Episodic air quality events aggravate short-term exposure
Wildfire smoke impacting the urban area
  The GAA has been affected by emissions from a wildfire event almost every summer since 2017
  The impact of the August 2021 wildfire lasted for over a week and led to extreme short-term PM2.5 levels (>300 μgm-3)
  Industrial accidents emitting hazardous pollutants
  In the recent years (2016-2020), there have been two large scale industrial accidents in plastic-recycling plants of the GAA
  Atmospheric dispersion carried the plumes over the Athens basin, leading to excessive PM levels, characterized by high BC contribution
  African dust intrusions
  Dust events due to Saharan dust transport are very common in Southern Greece, especially during spring, leading to extreme PM10 levels and also aggravating short-term PM2.5 exposure

## Slide 6: Identifying the special needs for AQ monitoring in metro areas
Large exposed populations necessitate spatially representative measurements, to capture within-area variability and reduce exposure misclassification error
Large areas mean that atmospheric dynamics can induce substantial intra-urban variability
The heterogeneous urban landscape and source mixture dictate measurement at different site types
Multiple stakeholders at different levels (governmental, regional, municipal, private sector) have different AQ management priorities and require solutions for local issues
Large investments required to expand regulatory network
Episodic events but also increased urban mobility call for near-real time information
Need for IoT integration and personalized exposure information (online platforms, smartphone apps, etc.)
While sensor-based solution will not substitute regulatory AQ monitoring stations for compliance assessment, it is imperative to calibrate their outputs for reliable results
Densify
Downsize
Integrate online
Calibrate

## Slide 7: Designing an integrated AQ monitoring network in Athens
Medium-cost AQ monitoring systems (<10000€)
Fixed-site regulatory AQ monitoring
(e.g. NOA - Thissio)
Low AQ monitoring systems(<1000€)
Gateway/Controller,
Data Server
Web Portal
Calibrated Data,
Air Quality Index,
Geospatial Info
Smartphone App
GSM
Wi-Fi
FTP
Calibration, evaluation
Design and implementation of an integrated ΙοΤ network and data-visualization platform
Products and services to inform and protect the public from excessive exposure
Incorporation of other available monitoring networks providing calibrated data

## Slide 8: Sensor-based monitoring instruments used by NOA in Athens
PurpleAir PA-II (PMS5003)
Low cost device, can be deployed in dense networks
Easy to install and operate, transmits data via Wi-Fi to an online platform
Real time monitoring (resolution ≈ 2 min)
Strong correlations with PM2.5 reference monitors (except in cases of dust)
Low-cost system for PM2.5 monitoring
Multi-pollutant systems for O3, NO2, CO and PM
AQMesh Multi-pollutant monitor
Alphasense electrochemical sensors for gas measurements, correcting for T interferences
Integrated in a user platform for data access and parametrization (3G transmission, API)
Real time monitoring (min. resolution = 5 min)
Strong correlations with CO, NO2 and O3 reference monitors

## Slide 9: Calibration of sensor-based systems at the NOA supersite
NOA urban background supersite in Thissio, central Athens
Concurrent operation with reference instruments using standard methods
Statistical evaluation of sensor performance
Linear models for correction of sensor outputs
Examination of T, RH effects and cross-pollutant interferences
Periodic calibration of sensors on-site (using golden-pods or the NOA mobile AQ monitoring station)

## Slide 10: The NOA/PANACEA PM2.5 monitoring network in Athens
https://air-quality.gr
PM2.5 monitoring in the GAA using low-cost sensors
26 measurement sites in the GAA
≈ 90 measurement sites in Greek cities
(in the framework of RI-PANACEA, with the cooperation of Greek Universities, such as UPatras)

## Slide 11: The NOA/EMISSION multi-pollutant monitoring network in Athens
O3, NOx, CO, PMx measurements in the GAA, using AQMesh and custom made low-cost systems
15 measurement sites
in the GAA
https://emission-web.meteo.noa.gr
Envi4Athens (DRAXIS)
- Smartphone app for the EMISSION network
- Personalized AQI and info - Citizen engagement

## Slide 12: An example: The August 2021 wildfire events
Start
of event
Nearing
the city
Covering
the basin

## Slide 13: The utility of a sensor-based network in the context of e-shape
Pilot: S2-P3: EO-based pollution-health risks profiling in the urban environment
Target: Blend EO platforms for AQ with socio-economic and health data, into an integrated risk assessment system to support decision making
Key tools:
    High-resolution, city-scale AQ modeling system (see upcoming presentation)
    Dynamic population exposure methodology
    Health impact assessment tools
Possibilities opened up with AQ monitoring in high resolution
    Improved validation and assimilation of the AQ modelling system
    Characterization of AQ at the municipality level
    Utilization of measurements in land-use regression models for spatial prediction of long-term exposure
    Provision of data for improved health impact assessment

## Slide 14: The path to an integrated network of calibrated data
Urban Traffic: 3
Urban Background: 15
Suburban Background: 13
Near-city Rural Background 2
Low-cost multi-pollutant systems
PM2.5 network
densification
Aim  Coverage at the municipality level

## Slide 15: Thank you !! ggrivas@noa.gr